## Slide 1: 天体测量学：地球参考系天球参考系 (TIRS-GCRS) 变换 (transforming coordinates from TIRS to GCRS)
2026-4-21
中山大学 珠海校区/教学大楼/珠海F206

## Slide 2: How can we transform station coordinates from the terrestrial to the celestial frame? [or the other way round …]
基于Michael Schindelegger的PPT

## Slide 3: Some motivation
Observations to/from objects in space:
Analyzing observations for certain target parameters requires transformation celestial ⟷ terrestrial frame
⟹ Consideration of Earth’s variable rotation
http://gpsx10.com/
https://www.gfz-potsdam.de
https://www.aulis.
com/laser.htm

## Slide 4: Outline
Contents of the lecture:
Earth rotation – an overview
Conventional reference systems
Transformation between celestial and terrestrial reference systems
Main reference: 1.李广宇
2. IERS Conventions (2010). Gérard Petit and Brian Luzum (eds.). (IERS Technical Note; 36) Frankfurt am Main: Verlag des Bundesamts für Kartographie und Geodäsie, 2010. 179 pp., ISBN 3-89888-989-6.
https://www.iers.org/IERS/EN/Publications/TechnicalNotes/tn36.html

## Slide 5: Overview
Three aspects of a variable rotation:
Earth‘s angular velocity is not constant
Orientation of the reference (e.g., rotation) axis varies with respect to space
Earth as a body changes its position with respect to this reference axis
5

## Slide 6: Why does the Earth not rotate …
… uniformly around an invariant axis?
The Earth‘s figure is not a sphere but rather corresponds to an oblate spheroid
Axes of rotation and maximum inertia (= figure axis) do not coincide
The Earth is neither rigid nor homogenous (deformations of solid parts, atmosphere, ocean, etc. …)

## Slide 7: Implications for …
Measurement of time
Positioning and navigation
 On Earth (1 𝑚𝑠 ≙ 45 𝑐𝑚 at the equator / 1 𝑚𝑎𝑠 ≙ 3 𝑐𝑚)
  In space: spacecraft tracking
Geodesy: reference frame, gravity field
Earth system research
Earth
surface
𝛼
𝑏 = 𝛼 𝑟𝑎𝑑 r
= 3 𝑐𝑚
Interaction and feedback effects:
  Ocean, atmosphere, cryosphere
  Mantle, Earth’s core
𝛼 = 1 𝑚𝑎𝑠
𝑏

## Slide 8: We seek quantities to describe …
The changing orientation of the rotation axis with respect to a celestial reference frame
→ precession/nutation
The changing position of the rotation axis relative to the body-fixed reference frame
→ polar motion
Variations in the rotation rate (= angular velocity) with respect to an atomic frequency standard
→ dUT1 (or ΔLOD)
⟹ 5 Earth Orientation Parameters

## Slide 9: Earth Orientation Parameters
Precession und nutation:
Response of the oblate Earth to luni-solar torques
Formal separation ⟶
Precession (long-period):
  Circular movement of rotation axis around ecliptic pole
  1 revolution in 25800 yr
Nutation (short-period):
  Smaller oscillations
Credit: Luciano Pederzoli

## Slide 10: Precession/nutation
10
9.2“ ≙ 276 m
6.9“ ≙ 83 m
50“/yr ≙
600 m/yr
Ecliptic North Pole
Trajectory of mean pole
Trajectory of true pole
Nutation ellipse
Precessional circle
Precession period also called Great” or “Platonic Year”
Nutation period with largest amplitude:
18.6 yr (Regression of the lunar node)

## Slide 11: Precession/nutation
P/N can be predicted almost perfectly ⟹
Typical series expansion:
{X, 𝑌} are two of the EOP and called nutation angles
18.6 𝑦𝑟

## Slide 12: Earth Orientation Parameters
Precession/Nutation ⟶ polar motion:
What is our reference axis?
Actual pole of rotation exhibits large short-term variability in the celestial frame ⟶ not suited
Reference
Pole (CIP)
Terrestrial
Frame
CIP – Celestial Intermediate Pole
Celestial Frame
𝑌 (nutation)
𝑿

## Slide 13: Earth Orientation Parameters
Reference Pole (CIP)
Terrestrial
Frame
𝑥𝑝 (polar motion)
𝑦𝑝
Precession/Nutation ⟶ polar motion:
Reality: we use a conventional reference pole = CIP
Intermediate pole in the eventual transformation
Polar motion angles {𝑥𝑝, 𝑦𝑝} also refer to CIP
Celestial
Frame

## Slide 14: Polar motion – Geophysical effects
„1st order“ pole trajectory:
Chandler Wobble
  Free oscillation of the Earth
  Period ∼ 433 days
Annual Wobble
  Forced oscillation, main driver (∼75%) are annual pressure over continental areas
14

Beat with a period of 6.3 yr and peak amplitudes of 9 m

## Slide 15: Polar motion – Geophysical effects
Secular polar motion:
Pole trajectory 1962.0 – 2010.7
(Linear) drift of the reference pole:
– 10 𝑐𝑚/𝑦𝑟 towards
78° W
  Main cause: glacial isostatic adjustment
Sudden changes since 2005 may have other causes (ice sheet melt, terrestrial water …)

## Slide 16: Earth Orientation Parameters
5th EOP ⟶ Variations in the rate of rotation
Understanding of time scales
required, particularly UT1 (Universal Time – corrected for polar motion effects)
Phase angle of a terrestrial object w.r.t. a reference point on a sphere
For more information, see: https://www.timeanddate.com/ti me/universal-time.html

Instantaneous phase angle
≙ UT1
0°/Gr.

## Slide 17: Universal Time – ΔLOD
Universal Time UT1, changes in length-of-day
Variations of the rotation rate can be expressed as deviations of UT1 from an atomic time scale (such as UTC) …
UT1-UTC = dUT1
… or as perturbations of the nominal rotation rate 1⁄86400 𝑠𝑒𝑐
ΔLOD (Excess of length-of-day)
Atomic frequency
standard
∆LOD = −
d
dt
dUT1
17

## Slide 18: Universal Time – ΔLOD
UT1-UTC < 0.9 s
leap seconds
ΔLOD (ms)
UT1-UTC without jumps
differentiation

## Slide 19: ΔLOD – Geophysical effects
Residuals are irregular or quasi-periodic …
Solid Earth tides
Ocean tides

## Slide 20: Outline
Contents of the lecture:
Earth rotation – an overview
Conventional reference systems
Transformation between celestial and terrestrial reference systems
Reference System ⟷ Reference Frame
Earth Orientation Parameters
X, 𝑌, 𝑥𝑝, 𝑦𝑝, dUT1

## Slide 21: Reference systems
International Terrestrial Reference System
ITRS is geocentric and co-rotates with the Earth
Unit length is the meter (SI)
Orientation of axes 𝑥, 𝑦, 𝑧
follows conventions:
Requirement that 𝑥, 𝑦, 𝑧 are aligned with a previous realization: BIH at epoch 1984.0
Arbitrary definition
Bureau International de l‘Heure (BIH) at Paris Observatory

## Slide 22: Reference systems
International Terrestrial Reference Frame
ITRF = realization of ITRS by virtue of positions and velocities of space-geodetic stations:
  ITRF94 ITRF96 … ITRF2008 ITRF2014
1499 observing stations at 975 sites

## Slide 23: Reference systems
Internat. Celestial Reference System/Frame
Both definition (ICRS) & realization (ICRF) constrained by stable “defining” radio sources:
ICRF2 (2009): 295 defining
ICRF3 (2018): 303 defining
Celestial coordinates of these sources observed with VLBI (Very Long Baseline Interferometry)

## Slide 24: Reference systems
https://flatearth.ws/stellar-aberration
https://phys.org/
Internat. Celestial Reference System/Frame
ICRS is barycentric, but in the following …
We assume that it is geocentric and the necessary corrections have been applied, e.g., aberration
Barycenter Geocenter

## Slide 25: Outline
Contents of the lecture:
Earth rotation – an overview
Conventional reference systems
Transformation between celestial and terrestrial reference systems
Previously: transformation based on ecliptic, vernal equinox , nutation in obliquity, …
Here: IAU 2000/2006 resolutions

## Slide 26: Transformation TRS ⟷ CRS
CIP
𝑸(𝑡)
W(𝑡)
𝘙(𝑡)
“Top view” of the IAU 2000 transformation
Involves intermediate system(s) that are tied to the CIP (see slide 12):
Pole of the CRS
Pole of the TRS
𝐶𝑅𝑆
= 𝑄 𝑡
𝑅 𝑡
W(𝑡)
T𝑅𝑆

## Slide 27: Transformation TRS ⟷ CRS
Rotation matrices account for …
(at a particular epoch)
In all clarity (before addressing some details):
Nutation Earth’s spin Polar motion
𝑄 𝑡 …
𝑅 𝑡 …
W(𝑡) …

## Slide 28: Transformation TRS ⟷ CRS
Non-rotating origins (NRO):
Kinematical definition, two NROs:
  Celestial Intermediate Origin (CIO) ⟶ takes over the role of the vernal equinox in the transformation
  Terrestrial Intermediate Origin (TIO)
NROs always on the equator of the CIP
Their positions depend on the history of CIP motion
CIP & respective NRO define 2 intermediate systems
  Celestial Intermediate Reference System (CIRS)
  Terrestrial Intermediate Reference System (TIRS)

## Slide 29: Transformation TRS ⟷ CRS
CIRS
Celestial Interm. Reference System
0: x-origin of ICRS
: auxiliary point on ICRS meridian
= NRO (CIO)
NRO in the CRS → CIO or , positioned on the CIP equator using the angle s

s
TIRS
 = TIO
σ0: the position of the CIO at J2000.0

## Slide 30: Transformation TRS ⟷ CRS
30
Coordinates of the CIP in CRS:
CIO Locator s:
 
dt  const
X t Y˙t  X˙ t Y t 
1 Z t 
t
s t  
t0
Precession/Nutation matrix:
𝑄 (𝑡) = 𝑅𝑧(−𝐸)𝑅𝑦(−𝑑)𝑅𝑧(𝐸 + 𝑠)


cos(𝐸) sin(𝐸)
X = sin 𝑑
𝑌 = sin 𝑑
𝑍 = cos(𝑑)
CIO 变换矩阵
该变换为天球中间参考系-天球参考系 (CIRS-GCRS) 变换.
CIP 向量e3’ 的经角 E 和余纬角 d

## Slide 31: 中间极和中间赤道在 GCRS 中的运动
CIP 向量e3’ 的方向由经角 E 和余纬角 d 确定，且满足方程
(e1, e2, e3)为 GCRS坐标轴单位向量
(e1’, e2’, e3’)为 CIRS坐标轴单位向量.
u , v 和 v’ 分别为交线和投影线单位向量
GCRS
(4.1)
31

## Slide 32: 中间极和中间赤道在 GCRS 中的运动
CIP 向量e3’ 连带中间赤道绕原点O的转动有两个分量: 1. 绕轴e3 ，角速度向量为 Ė e3 的转动; 2. 绕轴 u ， 角速度向量为 ḋ u 的转动
总角速度向量:
ω = Ė e3 + ḋ u (4.2)
GCRS
CIRS
代入上式 (4.1)
(4.3)
32

## Slide 33: 中间极和中间赤道在 GCRS 中的运动
ω1绕e3’ 轴(CIP)沿中间赤道经度方向的转动
GCRS
CIRS
(4.3)
ω2 是沿中间赤道纬度方向的转动
ω2
ω1
33

## Slide 34: 中间赤道上的无转动点 （CIO）
在中间赤道上取一点，假定它在天球系中转动的角速度向量为ω2 ，则它随着中间赤道在纬度方向一起转动，所以不会离开中间赤道
GCRS
CIRS
(4.3)
ω2
ω1
又不随着中间赤道绕 e3’ 轴在经向转动.
CIO
ICRS 指定GCRS 的基本方向 e1 尽可能接近历元平春分点
取e1’指向 CIO， 指定该基本方向构建CIRS
34

## Slide 35: Transformation TRS ⟷ CRS
Precession/Nutation matrix:
𝑄 (𝑡) = 𝑅𝑧(−𝐸)
CIO 变换矩阵
(e1 , e2) 在天球赤道面内绕第三轴 e3 逆时针旋转角 E
35

## Slide 36: Transformation TRS ⟷ CRS
Precession/Nutation matrix:
𝑄 (𝑡) = 𝑅𝑧(−𝐸)𝑅𝑦(−𝑑)
CIO 变换矩阵
(e3 , e1) 在垂直于交线的平面内绕第二轴 e2 逆时针旋转角 d
36

## Slide 37: Transformation TRS ⟷ CRS
Precession/Nutation matrix:
𝑄 (𝑡) = 𝑅𝑧(−𝐸)𝑅𝑦(−𝑑)𝑅𝑧(𝐸 + 𝑠)
CIO 变换矩阵
(e1 , e2)在中间赤道面内绕中间极向量 e3 顺时针旋转角 E + s
37

## Slide 38: Transformation TRS ⟷ CRS
𝐸𝑅𝐴 … Earth Rotation Angle
𝐸𝑅𝐴 proportional to dUT1, only input
UT1-UTC
Earth rotation matrix:
𝑅(𝑡) = 𝑅𝑧(−𝐸𝑅𝐴)
𝐸𝑅𝐴 𝑇𝑢 = 2𝜋 0.7790572732640 + 1.00273781191135448 𝑇𝑢
𝑇𝑢 = mjd UT1 epoch − 51544.5
Modified Julian Date of the observation epoch, e.g., 1.9.2020, 16:00 UTC:
mjd 1.9.2020 = 59093
mjd UT1 epoch = 59093 + 16/24 + 𝑑𝑈𝑇1/24x3600

## Slide 39: Transformation TRS ⟷ CRS

s'
NRO in the TRS → TIO or , positioned on the CIP equator using the angle s'
Terrestrial Interm. Reference System
TIRS
0: x-origin of ITRS
: auxiliary point on the ITRS meridian
= NRO (TIO)

## Slide 40: Transformation TRS ⟷ CRS

s'
= NRO (TIO)
Polar motion matrix:
W(𝑡) = 𝑅𝑧(−𝑠')𝑅𝑦(𝑥𝑝)𝑅𝑥(𝑦𝑝)
TIO Locator s' reflecting CIP history (usually negligible):
dt
t
s  
t0

2
xp y˙ p  x˙p yp

## Slide 41: Transformation TRS ⟷ CRS
Summary:
Five Earth Orientation Parameters
Their physical meaning and practical relevance
Importance of (global) reference systems
Astrometry sub-routines:
  https://www.iausofa.org/current-software (SOFA)
  NOVAS (Naval Observatory Vector Astrometry Subroutines), in C/Fortran/Python